### iDrac Dell
IPMI es un estándar que encontramos en el hardware de muchos servidores, se trata de un chipset que permite obtener información del estado de diferentes componentes hardware, temperaturas, voltajes, etc. Este estándar lo conforman empresas como HP, Dell e Intel.
Ejemplo de como activarlo desde el SSH de iDrac 6
racadm config -g cfgIpmiLan -o cfgIpmiLanEnable 1
racadm config -g cfgIpmiLan -o cfgIpmiLanPrivilegeLimit <nivel>
donde <nivel> es uno de los siguientes valores:
- 2 (Usuario)
- 3 (Operador)
- 4 (Administrador)
Como ver la configuración actual
racadm getconfig -g cfgIpmiLan
http://support.dell.com/support/edocs/software/smdrac3/idrac/idrac1.11/sp/ug/chap09.htm?~file=/software/smdrac3/idrac/idrac1.11/sp/ug/chap09.htm&~f=
Como obtener los datos desde nuestro sistema operativo
ipmitool -I lan -H 10.0.0.10 -U user -P pass chassis status
ipmitool -I lan -H 10.0.0.10 -U user -P pass sdr list
ipmitool -I lan -H 10.0.0.10 -U user -P pass sdr type "Power Supply"
Status | 64h | ok | 10.1 | Presence detected
Status | 65h | ok | 10.2 | Presence detected, Power Supply AC lost
Status | 66h | ok | 10.3 | Presence detected
Status | 67h | ok | 10.4 | Presence detected
PS Redundancy | 74h | ok | 7.1 | Redundancy Degraded
/usr/sbin/ipmimonitoring -h 10.15.3.107 --config-file /etc/freeipmi.conf -u user -p pass
Record_ID	Sensor Name	Sensor Group	Monitoring Status	Sensor Units	Sensor Reading
12	Ambient Temp	Temperature	Nominal	C	25.000000
22	CMOS Battery	Battery	Nominal	N/A	'OK'
24	VCORE PG	Voltage	Nominal	N/A	'State Deasserted'
25	VCORE PG	Voltage	Nominal	N/A	'State Deasserted'
26	VCORE	Voltage	Nominal	N/A	'State Deasserted'
27	VCORE	Voltage	Nominal	N/A	'State Deasserted'
28	VCACHE PG	Voltage	Nominal	N/A	'State Deasserted'
29	VCACHE PG	Voltage	Nominal	N/A	'State Deasserted'
30	VCACHE	Voltage	Nominal	N/A	'State Deasserted'
31	VCACHE	Voltage	Nominal	N/A	'State Deasserted'
32	VIO PG	Voltage	Nominal	N/A	'State Deasserted'
33	VIO PG	Voltage	Nominal	N/A	'State Deasserted'
34	CPU 1.8 PLL PG	Voltage	Nominal	N/A	'State Deasserted'
35	8V Rear PG	Voltage	Nominal	N/A	'State Deasserted'
36	8V Front PG	Voltage	Nominal	N/A	'State Deasserted'
37	5V Rear PG	Voltage	Nominal	N/A	'State Deasserted'
38	5V Front PG	Voltage	Nominal	N/A	'State Deasserted'
39	3.3V PG	Voltage	Nominal	N/A	'State Deasserted'
40	1.8V PG	Voltage	Nominal	N/A	'State Deasserted'
41	1.5V PG	Voltage	Nominal	N/A	'State Deasserted'
42	1.1V PG	Voltage	Nominal	N/A	'State Deasserted'
43	0.9V PG	Voltage	Nominal	N/A	'State Deasserted'
44	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
45	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
46	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
47	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
48	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
49	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
50	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
51	Mem VR PG	Voltage	Nominal	N/A	'State Deasserted'
52	VR PG	Voltage	Nominal	N/A	'State Deasserted'
53	VR1 PG	Voltage	Nominal	N/A	'State Deasserted'
54	VR2 PG	Voltage	Nominal	N/A	'State Deasserted'
58	Heatsink Pres	Entity Presence	Nominal	N/A	'Entity Present'
59	iDRAC6 Ent Pres	Entity Presence	Nominal	N/A	'Entity Present'
60	USB Cable Pres	Entity Presence	Nominal	N/A	'Entity Present'
61	Stor Adapt Pres	Entity Presence	Nominal	N/A	'Entity Present'
62	PCIe Riser Pres	Entity Presence	Critical	N/A	'Entity Absent'
63	IO Riser Pres	Entity Presence	Nominal	N/A	'OK'
64	FAN 1 RPM	Fan	Nominal	RPM	2400.000000
65	FAN 2 RPM	Fan	Nominal	RPM	2400.000000
66	FAN 3 RPM	Fan	Nominal	RPM	2400.000000
67	FAN 4 RPM	Fan	Nominal	RPM	2760.000000
68	FAN 5 RPM	Fan	Nominal	RPM	2640.000000
69	FAN 6 RPM	Fan	Nominal	RPM	2640.000000
74	Presence	Entity Presence	Nominal	N/A	'Entity Present'
75	Presence	Entity Presence	Nominal	N/A	'Entity Present'
76	Presence	Entity Presence	Nominal	N/A	'Entity Present'
77	Presence	Entity Presence	Nominal	N/A	'Entity Present'
78	Presence	Entity Presence	Nominal	N/A	'Entity Present'
79	Presence	Entity Presence	Nominal	N/A	'Entity Present'
80	Presence	Entity Presence	Nominal	N/A	'Entity Present'
81	Presence	Entity Presence	Nominal	N/A	'Entity Present'
82	Presence	Entity Presence	Nominal	N/A	'Entity Present'
83	Status	Processor	Nominal	N/A	'Processor Presence detected'
84	Status	Processor	Nominal	N/A	'Processor Presence detected'
85	Status	Processor	Nominal	N/A	'Processor Presence detected'
86	Status	Processor	Nominal	N/A	'Processor Presence detected'
87	Status	Power Supply	Nominal	N/A	'Presence detected'
88	Status	Power Supply	Nominal	N/A	'Presence detected'
89	Status	Power Supply	Nominal	N/A	'Presence detected'
90	Status	Power Supply	Nominal	N/A	'Presence detected'
91	Current	Current	Nominal	A	0.800000
92	Current	Current	Nominal	A	0.880000
93	Current	Current	Nominal	A	0.680000
94	Current	Current	Nominal	A	0.800000
95	Voltage	Voltage	Nominal	V	222.000000
96	Voltage	Voltage	Nominal	V	224.000000
97	Voltage	Voltage	Nominal	V	224.000000
98	Voltage	Voltage	Nominal	V	222.000000
99	Riser Config	Cable/Interconnect	Nominal	N/A	'Cable/Interconnect is connected'
100	OS Watchdog	Watchdog 2	Nominal	N/A	'OK'
102	Intrusion	Physical Security	Nominal	N/A	'OK'
103	PS Redundancy	Power Supply	Nominal	N/A	'Fully Redundant'
104	Fan Redundancy	Fan	Nominal	N/A	'Fully Redundant'
105	System Level	Current	Nominal	W	700.000000
107	Drive	Drive Slot	Nominal	N/A	'Drive Presence'
109	Cable SAS A	Cable/Interconnect	Nominal	N/A	'Cable/Interconnect is connected'

Si queremos elegir mostrar solo uno de los grupos deberemos agregar a la linea de comandos la opcion -g y el número -g 103.
Record_ID	Sensor Name	Sensor Group	Monitoring Status	Sensor Units	Sensor Reading
103	PS Redundancy	Power Supply	Nominal	N/A	'Fully Redundant'

Ejemplo consultar el Voltage y separalo en ;
ipmimonitoring -h 10.1.1.7 --config-file /usr/local/nagios/etc/ipmi/freeipmi-esxi.conf --quiet-cache --sdr-cache-recreate -s 95,96,97,98 -g Voltage |tail -n 4 | cut -d "|" -f 6 | sed -e 's/^[ \t]*/Voltage=/' | sed ':a;N;$!ba;s/\n/ /g' | sed -e 's/ /;/g'| sed -e 's/^[ \t]*//' Voltage=218.000000;Voltage=220.000000;Voltage=218.000000;Voltage=218.000000