# FortiAP
### Administración
Ejemplo de configuración de IP y de controlador Wireless
cfg -a ADDR_MODE=STATIC
cfg -a AP_IPADDR=192.168.1.100
cfg -a AP_NETMASK=255.255.255.0
cfg -a IPGW=192.168.1.1
cfg -a AC_DISCOVERY_TYPE=1
cfg -a AC_IPADDR_1=192.168.1.155
cfg -c
### FortiAP CLI
http://help.fortinet.com/fos50hlp/54/Content/FortiOS/fortigate-wireless-54/reference-fortiap-cli.htm
The FortiAP CLI controls radio and network operation through the use of variables manipulated with the cfg command. There are also diagnostic commands.
The cfg command include the following
cfg -s	List variables.
cfg -a var=value	Add or change a variable value.
cfg -c	Commit the change to flash.
cfg -x	Reset settings to factory defaults.
cfg -r var	Remove variable.
cfg -e	Export variables.
cfg -h	Display help for all commands.

The configuration variables are:
Var	Description and Values
AC_CTL_PORT	WiFi Controller control (CAPWAP) port. Default 5246.
AC_DATA_CHAN_SEC	Data channel security.0 - Clear text1 - DTLS (encrypted)2 - Accept either DTLS or clear text (default)
AC_DISCOVERY_TYPE	1 - Static. Specify WiFi Controllers2 - DHCP3 - DNS5 - Broadcast6 - Multicast0 - Cycle through all of the discovery types until successful.
AP_IPADDRAP_NETMASKIPGW	These variables set the FortiAP unit IP address, netmask and default gateway when ADDR_MODE is STATIC.Default 192.168.1.2 255.255.255.0, gateway 192.168.1.1.
AC_HOSTNAME_1AC_HOSTNAME_2AC_HOSTNAME_3	WiFi Controller host names for static discovery.
AC_IPADDR_1AC_IPADDR_2AC_IPADDR_3	WiFi Controller IP addresses for static discovery.
AC_DISCOVERY_DHCP_OPTION_CODE	Option code for DHCP server. Default 138.
AC_DISCOVERY_MC_ADDR	Multicast address for controller discovery. Default 224.0.1.140.
ADDR_MODE	How the FortiAP unit obtains its IP address and netmask.DHCP - FortiGate interface assigns address.STATIC - Specify in AP_IPADDR and AP_NETMASK.Default is DHCP.
ADMIN_TIMEOUT	Administrative timeout in minutes. Applies to Telnet and web-based manager sessions. Default is 5 minutes.
AP_MGMT_VLAN_ID	Non-zero value applies VLAN ID for unit management. Default: 0.
AP_MODE	FortiAP operating mode.0 - Thin AP (default)2 - Unmanaged Site Survey mode. See SURVEY variables.
BAUD_RATE	Console data rate: 9600, 19200, 38400, 57600, or 115200 baud.
DNS_SERVER	DNS Server for clients. If ADDR_MODE is DHCP the DNS server is automatically assigned.
FIRMWARE_UPGRADE	Default is 0.
HTTP_ALLOW	Access to FortiAP web-based manager1 - Yes (default), 0 - No.
LED_STATE	Enable/disable status LEDs.0 - LEDs enabled, 1 - LEDs disabled, 2 - follow AC setting.
LOGIN_PASSWD	Administrator login password. By default this is empty.
STP_MODE	Spanning Tree Protocol. 0 is off. 1 is on.
TELNET_ALLOW	By default (value 0), Telnet access is closed when the FortiAP unit is authorized. Set value to 1 to keep Telnet always available.
WTP_LOCATION	Optional string describing AP location.
Mesh variables
MESH_AP_TYPE	Type of communication for backhaul to controller:0 - Ethernet (default)1 - WiFi mesh2 - Ethernet with mesh backup support
MESH_AP_SSID	SSID for mesh backhaul. Default: fortinet.mesh.root
MESH_AP_BSSID	WiFi MAC address
MESH_AP_PASSWD	Pre-shared key for mesh backhaul.
MESH_ETH_BRIDGE	1 - Bridge mesh WiFi SSID to FortiAP Ethernet port. This can be used for point-to-point bridge configuration. This is available only when MESH_AP_TYPE =1.0 - No WiFi-Ethernet bridge (default).
MESH_MAX_HOPS	Maximum number of times packets can be passed from node to node on the mesh. Default is 4.
The following factors are summed and the FortiAP associates with the lowest scoring mesh AP.
MESH_SCORE_HOP_WEIGHT	Multiplier for number of mesh hops from root. Default 50.
MESH_SCORE_CHAN_WEIGHT	AP total RSSI multiplier. Default 1.
MESH_SCORE_RATE_WEIGHT	Beacon data rate multiplier. Default 1.
MESH_SCORE_BAND_WEIGHT	Band weight (0 for 2.4GHz, 1 for 5GHz) multiplier. Default 100.
MESH_SCORE_RSSI_WEIGHT	AP channel RSSI multiplier. Default 100.
Survey variables
SURVEY_SSID	SSID to broadcast in site survey mode (AP_MODE=2).
SURVEY_TX_POWER	Transmitter power in site survey mode (AP_MODE=2).
SURVEY_CH_24	Site survey transmit channel for the 2.4Ghz band (default 6).
SURVEY_CH_50	Site survey transmit channel for the 5Ghz band (default 36).
SURVEY_BEACON_INTV	Site survey beacon interval. Default 100msec.

Diagnose commands include:
cw_diag help	Display help for all diagnose commands.
cw_diag uptime	Show daemon uptime.
cw_diag –tlog <on|off>	Turn on/off telnet log message.
cw_diag –clog <on|off>	Turn on/off console log message.
cw_diag baudrate [9600 | 19200 | 38400 | 57600 | 115200]	Set the console baud rate.
cw_diag plain-ctl [0|1]	Show or change current plain control setting.
cw_diag sniff-cfg ip port	Set sniff server ip and port.
cw_diag sniff [0|1|2]	Enable/disable sniff packet.
cw_diag stats wl_intf	Show wl_intf status.
cw_diag admin-timeout [30]	Set shell idle timeout in minutes.
cw_diag -c wtp-cfg	Show current wtp config parameters in control plane.
cw_diag -c radio-cfg	Show current radio config parameters in control plane.
cw_diag -c vap-cfg	Show current vaps in control plane.
cw_diag -c ap-rogue	Show rogue APs pushed by AC for on-wire scan.
cw_diag -c sta-rogue	Show rogue STAs pushed by AC for on-wire scan.
cw_diag -c arp-req	Show scanned arp requests.
cw_diag -c ap-scan	Show scanned APs.
cw_diag -c sta-scan	Show scanned STAs.
cw_diag -c sta-cap	Show scanned STA capabilities.
cw_diag -c wids	Show scanned WIDS detections.
cw_diag -c darrp	Show darrp radio channel.
cw_diag -c mesh	Show mesh status.
cw_diag -c mesh-veth-acinfo	Show mesh veth ac info, and mesh ether type.
cw_diag -c mesh-veth-vap	Show mesh veth vap.
cw_diag -c mesh-veth-host	Show mesh veth host.
cw_diag -c mesh-ap	Show mesh ap candidates.
cw_diag -c scan-clr-all	Flush all scanned AP/STA/ARPs.
cw_diag -c ap-suppress	Show suppressed APs.
cw_diag -c sta-deauth	De-authenticate an STA.